## Slide 1
North Carolina Ratepayer Savings from Solar
Prepared for NCSEA
September 23, 2026
Angela Zeng, Pat Knight, Selma Sharaf, Caroline Resor

## Slide 2
Contents
Introduction
Methodology
Findings
Appendices

## Slide 3
Introduction

## Slide 4: Executive summary
We found that solar became cost-effective over time. Solar deployed in North Carolina has had net costs of $401 million to date for ratepayers across all customer classes. Since 2022, solar has saved ratepayers $339 million compared to gas and coal.1
Our analysis indicates that solar is likely to become even more cost-effective over the next 10 years. We estimate that solar will produce $2.4 billion in net savings over the next 10 years.2
Ratepayer Savings in North Carolina
Synapse analyzed historical ratepayer bill impacts from solar energy resource additions driven by Senate Bill 3 (SB3) and the Public Utility Regulatory Policies Act (PURPA) in North Carolina between 2007 and 2025 and forecasted future savings through 2035.
Since 2022, for every $1 ratepayers spent on solar, they saved $1.16
All-in cost comparison between fossil resources and solar3
(1) All results are presented in 2025 dollars unless otherwise noted. (2) This includes existing solar and new builds estimated over the next 10 years to meet an extension of the Clean Energy and Energy Efficiency Portfolio Standard (CEPS) and the Duke Advancing Development Load forecast. (3) Costs are only available in 2009 and later years, as our database does not include any solar projects that were operational in 2007-2008.

## Slide 5: Analytical purpose
To understand the economic impact of the Public Utility Regulatory Policies Act (PURPA) and Senate Bill 3 (SB3) on ratepayer bills in North Carolina, Synapse conducted:
  A historical analysis of ratepayer impacts from renewable resource additions, specifically solar, driven by these policies from 2007–2025.
  A forward-looking analysis estimating the potential impacts through 2035, assuming additional solar to make progress towards North Carolina’s 2050 carbon neutrality target.1
In both analyses, we quantified the relevant solar capacity and modeled its lifecycle costs and benefits, comparing them to counterfactual in which loads were met with coal and natural gas generation instead. We then calculated net ratepayer bill impacts.
Ratepayer Savings in North Carolina
North Carolina’s solar policy
PURPA requires utilities to purchase energy and capacity from approved generators known as Qualifying Facilities at avoided cost rates.
SB3 in 2007 required Duke Energy Carolinas and Duke Energy Progress to meet a percentage of retail electricity sales with qualifying renewable energy or energy efficiency resources by creating a Renewable Energy and Energy Efficiency Portfolio Standard (REPS).2
These two procurement pathways have enabled solar, wind, and other renewable capacity to come online and displace generation from fossil plants.
(1) We did not evaluate beyond 2035. We estimated the annual renewable energy generation through 2035 needed to meet North Carolinas’s 2050 carbon neutrality target and assume the Clean Energy and Energy Efficiency Portfolio Standard (CEPS) requirement will increase linearly from 12.5 percent in 2027 to 100 percent in 2050. (2) In 2023, Senate Bill 678 amended REPS by expanding it to be CEPS.

## Slide 6
Methodology

## Slide 7: Quantifying historical ratepayer impacts of solar
Solar capacity
PURPA and SB3 facilitated the installation of 6.1 GW of solar by 2025. We sorted the MW based on how they were compensated.1,2
Ratepayer Savings in North Carolina
Qualifying Facility
Utility-owned
Standard Offer Contract
Competitively procured (PPA)
Merchant
(1) This excludes solar in Dominion’s service territory. There were no projects installed in 2007 or 2008. Prior to HB 589 in 2017, facilities under 5 MW were eligible for a Standard Offer Contract. After 2017, facilities under 1 MW were eligible. We used NCSEA’s Market Intelligence Hub to classify MW as Standard Offer Contract or not using facility size, contract length, and installation year. (2) Market Intelligence Hub, Renewable Energy Database. NCSEA. (3) Compensation was at a fixed long-term rate during the contract term and variable rate after. We assume a solar PV lifetime of 25 years. (4) We estimated REC costs using data in the annual REPS reports. Available at: https://www.ncuc.gov/Reps/reps.html. (5) PV PPA prices. Lawrence Berkeley Lab. Available at: https://emp.lbl.gov/pv-ppa-prices. (6) We used a fixed-tilt PV capacity factor to calculate generation. Available at https://emp.lbl.gov/pv-capacity-factors.
Solar costs
Certain Qualifying Facilities received Standard Offer Contracts and were compensated at published avoided cost rates.3 We found that 39 percent (by MW) were compensated at the avoided cost rate. The solar integration services charge is embedded in the avoided cost rate. These MW also incurred REC costs.4
We assumed that all other solar project MW were compensated at a PPA rate.5
For each year and compensation category, we multiplied the MWh by the per MWh costs to determine the total cost.6
Types of solar projects
Compensation:
Avoided cost rate
PPA rate

## Slide 8: Estimating future ratepayer impacts of solar
Ratepayer Savings in North Carolina
(1) 2025 Carolinas Resource Plan. Duke Energy. Available at: https://www.duke-energy.com/our-company/about-us/irp-carolinas/2025-crp. (2) Clean Energy and Energy Efficiency Portfolio Standard (CEPS). North Carolina Utilities Commission. Available at: https://www.ncuc.gov/Reps/reps.html. (3) Based on the decline in new QF solar capacity since HB 589, we assumed that new solar would be compensated at a PPA rate.
Solar capacity
We estimated the annual renewable energy generation through 2035 needed to meet North Carolina’s 2050 carbon neutrality target, using Duke’s Advancing Development Load forecast and assuming the CEPS requirement will increase linearly from 12.5 percent in 2027 to 100 percent in 2050.1,2
We assumed that any new project capacity built to meet the generation target would come from solar. We found that 27 GW of solar would be needed over 2028–2035 to meet the generation target.
Solar costs
We assumed that future solar projects will be compensated at the PPA rate.3
For each year, we multiplied the estimated solar project MWh by the PPA rate to determine the total cost.

## Slide 9: Quantifying historical avoided coal and gas costs
Ratepayer Savings in North Carolina
Fuel costs. Solar generation avoided the need for some generation from coal and gas resources. We quantified the historical solar generation, determined the makeup of the avoided generation (coal versus gas), and applied historical heat rates and fuel costs to determine the total avoided fuel costs.1,2
Operations and maintenance costs. Solar generation avoided some operation and maintenance (O&M) costs at coal and gas power plants. We estimated the share of solar generation that would have been met via gas versus coal each year and then multiplied each by the historical O&M costs for a gas combined cycle or coal plant, respectively, to calculate total avoided O&M costs.3
Capital costs. Solar projects provided a limited amount of firm capacity to the grid, avoiding the equivalent firm capacity that would have been provided by new gas combustion turbine (CT) projects or market capacity purchases.4 We multiplied these MW of firm capacity provided by solar by typical gas CT capital costs to calculate total avoided capital costs.5, 6
Installed solar projects avoided the need for a certain amount of coal and gas plant costs.
(1) Form 923. Energy Information Administration. Available at: https://www.eia.gov/electricity/data/eia923/. (2) AVERT. Available at: https://www.epa.gov/avert/avoided-emission-rates-generated-avert. (3) LCOE Report Version 15.0 (2021). Lazard. Available at: https://www.lazard.com/research-insights/levelized-cost-of-energy-levelized-cost-of-storage-and-levelized-cost-of-hydrogen-2021/. (4) Duke Energy Carolinas and Duke Energy Progress Effective Load Carrying Capability (ELCC) Report. November 2025. Available at: https://dms.psc.sc.gov/Attachments/Matter/0fddc6ef-dd6e-431c-b4e0-1a3b93bb1148. (5) LCOE Reports Versions 9.0 and 11.0-19.0 (2015, 2017-2026). Lazard. (6) Electricity Annual Technology Baseline. National Laboratory of the Rockies. 2024. Available at: https://atb.nlr.gov/electricity/2024/data.

## Slide 10: Estimating future avoided coal and gas costs
Ratepayer Savings in North Carolina
Fuel costs. To estimate avoided fuel costs, we first calculated avoided future coal and gas generation using our forward-looking solar generation trajectory, holding the 2025 fuel mix constant.1 We then applied 2025 heat rate assumptions and fuel price projections to estimate total avoided fuel costs.2, 3
Operations and maintenance costs. Similar to the historical analysis, we estimated the share of solar generation that would otherwise be met via gas versus coal each year and then multiplied each by historical O&M costs for a gas combined cycle or coal plant, respectively, to calculate total avoided O&M costs.3 We used historical costs because fossil plant O&M costs tend to remain relatively flat over time.
Capital costs. Solar projects will provide some amount of firm capacity to the grid, avoiding the equivalent firm capacity that would otherwise be provided by new gas CT projects or market capacity purchases.4 We multiplied the MW of firm capacity provided by solar by typical gas CT capital costs, holding the 2026 capital cost constant, to calculate total avoided capital costs.5, 6
Solar installed between now and 2035 will avoid the need for a certain amount of coal and gas plant costs.
(1) AVERT. Available at: https://www.epa.gov/avert/avoided-emission-rates-generated-avert. (2) AEO 2026 Table 3.5 (South-Atlantic). Energy Information Administration. Available at: https://www.eia.gov/outlooks/aeo/tables_ref.php (3) Form 923. Energy Information Administration. Available at: https://www.eia.gov/electricity/data/eia923/. (4) LCOE Report Version 15.0 (2021). Lazard. Available at: https://www.lazard.com/research-insights/levelized-cost-of-energy-levelized-cost-of-storage-and-levelized-cost-of-hydrogen-2021/. (5) Duke Energy Carolinas and Duke Energy Progress Effective Load Carrying Capability (ELCC) Report. November 2025. Available at: https://dms.psc.sc.gov/Attachments/Matter/0fddc6ef-dd6e-431c-b4e0-1a3b93bb1148. (6) LCOE Reports Versions 9.0 and 11.0-19.0 (2015, 2017-2026). Lazard. (7) Electricity Annual Technology Baseline. National Laboratory of the Rockies. 2024. Available at: https://atb.nlr.gov/electricity/2024/data.

## Slide 11
Findings

## Slide 12: As solar ramped up, it became cheaper
It took a few years, but solar installations grew dramatically, with 6.1 GW of new solar installed in North Carolina by 2025.
The per MWh cost of solar decreased, rivaling the cost of fossil resources. Since 2022, solar has been the cheaper option.
Generation from solar increased, displacing more gas and coal generation – and associated gas and coal costs.
Ratepayer Savings in North Carolina
Note: Battery storage capacity from Form 860. Energy Information Administration. Available at https://www.eia.gov/electricity/data/eia860/.

## Slide 13: Solar is now providing ratepayers net benefits
Ratepayer Savings in North Carolina
All-in solar compared to gas and coal costs by year
We compared solar costs to the gas and coal costs ratepayers would have incurred without the presence of solar each year.
Over 2007–2025, solar costs totaled $5.3 billion and displaced costs from gas and coal totaled $4.9 billion. Solar had net costs of $401 million.1
One of the advantages of solar is that it does not have fuel costs or experience fuel price volatility due to weather or geopolitical events.
(1) This is inclusive of all customer classes.
Since 2022, solar has saved ratepayers $339 million compared to gas and coal. During that period, for every $1 spent on solar, ratepayers saved $1.16.

## Slide 14: In addition to offering savings, solar avoids fuel price volatility
High reliance on natural gas can lead to rate and bill volatility since gas prices respond to weather events such as winter storms and geopolitical events such Russia’s invasion of Ukraine. Solar, which does not have fuel costs, avoids this volatility.
Ratepayer Savings in North Carolina
Historical Henry Hub natural gas price fluctuations, 2009–20261
Natural gas delivered to North Carolina, 2018–2024:2
Half the time, the month-to-month variation in gas prices was at least 10 percent
Ten percent of the time, the month-to-month variation was at least 30 percent
(1) Henry Hub Natural Gas Spot Price. Energy Information Administration. Available at: https://www.eia.gov/dnav/ng/hist/rngwhhdm.htm
(2) North Carolina Natural Gas Price Sold to Electric Power Consumers . Energy Information Administration. Available at: https://www.eia.gov/dnav/ng/hist/n3045nc3m.htm

## Slide 15: We estimate that solar will continue to save ratepayers money
Our analysis indicates that solar is likely to become even cheaper, producing $2.4 billion in net savings over the next 10 years compared to meeting load with coal and gas.1
We estimate that North Carolina utilities can build 4 GW per year of solar cost-effectively and stay in step with CEPS.
Our analysis indicates that a smaller amount of solar built would also be cost-effective.
Incremental solar capacity through 2035
Net savings from solar by year
All-in cost comparison between fossil resources and solar
(1) This is inclusive of all customer classes.
Ratepayer Savings in North Carolina

## Slide 16: Customer bills are now lower because of solar
Since 2022, solar has saved all ratepayers money.1
Solar produced net savings of $38 million per year on average across residential customers, equivalent to $8 of savings per residential customer per year.
Solar produced net savings of $47 million per year on average across C&I customers.
Ratepayer Savings in North Carolina
From now through 2035, we estimate that solar will continue to save all ratepayers money.2
Solar may produce net savings of $77 million per year on average across residential customers, equivalent to $13 of savings per residential customer per year.
Solar may produce net savings of $167 million per year on average across C&I customers.
Over 2007–2021, the cost of solar outweighed the displaced gas and coal costs.
Solar produced net costs of $25 million per year on average across residential customers, equivalent to $6 per residential customer per year.
Solar produced net costs of $32 million per year on average across commercial & industrial (C&I) customers.
(1) Solar has saved money for every customer class. Our analysis includes customers in Duke Energy’s North Carolina service territory as well as North Carolina’s municipal and cooperative utility service territories. (2) Our analysis did not evaluate beyond 2035; solar may continue to produce savings for all ratepayers beyond this timeframe.

## Slide 17
Appendices

## Slide 18: Methods detail: Estimating future solar capacity
Ratepayer Savings in North Carolina
We projected the North Carolina CEPS requirement by drawing a straight line from 12.5 percent in 2027 to 100 percent (carbon neutral) in 2050 to meet North Carolina’s 2050 carbon neutrality target.
We multiplied the CEPS requirement by Duke’s Advancing Development Load forecast to determine the required clean energy generation.
We assumed that any new project capacity built to meet the generation target would come from solar.
We then calculated the annual incremental solar capacity.
Forecasted solar generation through 2035

## Slide 19: Methods detail: Quantifying historical avoided coal and gas costs
Ratepayer Savings in North Carolina
(1) We did not explicitly estimate avoided transmission and distribution (T&D) costs. Depending on a host of variables, solar can increase T&D costs or avoid them.
Fuel costs
  We quantified the historical solar generation because this equals the gas and coal generation that solar displaced. We applied a degradation rate and a capacity factor to the historical solar capacity to determine the solar generation (MWh) in each operating year.
  For resources on the margin, we determined the share that was gas versus coal in each year using AVERT.
  We calculated the annual average gas and coal fuel costs in North Carolina using data from EIA Form 923.
  We applied historical annual heat rates from For 923 to determine total avoided fuel costs.
Fixed and variable operations and maintenance costs
  We estimated the share of avoided generation from solar that would have likely been met by gas versus coal in each year using AVERT.
  We applied the average $/MWh gas combined cycle and coal fixed operations and maintenance and variable operations and maintenance costs from the Lazard levelized cost of energy (LCOE) Report Version 15.0 (2021) to calculate total costs.
Capital costs
  We assumed that all firm solar capacity would have been met with gas.
  We assumed an average solar effective load carrying capacity (ELCC) of 9 percent (based on the November 2025 Duke Energy ELCC report.
  We use the annual $/kW-yr gas combustion turbine (CT) capital cost from the Lazard LCOE Report Version 15.0.
  We applied a 7 percent levelization factor based on the National Lab of the Rockies 2024 Annual Technology Baseline (ATB) report’s Capital Recovery Factor for utility-scale PV.